## Slide 1: Understanding and Using Geometry, Projections and Spatial Reference Systems in ArcGIS
Rob Juergens, Melita Kennedy, Annette Locke

## Slide 2: Introduction
We present fundamental concepts necessary for the correct and efficient use of geometry and spatial reference APIs
Geometry types
Spatial references and their properties
How spatial references and geometries interact
Notes: Purpose
Not to teach you how to code
Our libs low-level with many APIs built on top of them
To give basic understanding of spatial references and geometry

## Slide 3: Geometry

## Slide 4: What is a geometry?
Defines the shape of a feature
Vector representation for top level types
In other words, vertices have x, y coordinates
Optional z- (height) and m- (measure)

## Slide 5: Working with and analyzing geometries
Simple geometry verification
  Adhere to a set of rules
Topological operations
  For example, Buffer, Symmetric Difference, Union, Intersection
Relational operations
  For example, Disjoint, Touches, Overlaps, Crosses, Within

## Slide 6: Points
Building blocks for all geometries

## Slide 7: Multipoints
Each multipoint feature is a collection of points

## Slide 8: Polylines
Elliptical
Arc
Points are used to build segments
Composed of paths
Composed of segments
Segments can be four types
Polyline
Paths
Line
Bézier
Curve
Circular
Arc
Points
Segments
A collection of paths

## Slide 9: Polylines
Single part
Multipart
Notes: Single part
  1 paths, 5 segments
Multipart
  2 paths, 4 segments & 3 segments

## Slide 10: Polygons
Elliptical
Arc
Points are used to build segments
Composed of rings
Composed of closed segments
Segments can be four types
Polygon
Rings
Line
Bézier
Curve
Circular
Arc
Points
Segments
A collection of rings

## Slide 11: Polygons
Inner ring
Outer ring

## Slide 12: Non-simple Polygons

## Slide 13: Simple Polygons
Notes: Simplifying may add or remove vertices.

## Slide 14: So what? Why do we care if geometries are simple?
Cannot rely on results from operations using non-simple geometries
Get an error
Get incorrect results

## Slide 15: Why do we care if geometries are simple?
Demo
Notes: Using a Geometry Service back in Redlands
Non-simple polygon, self-intersects
Query parcels contained by polygon
Simplify into a three-part feature then query

## Slide 16: Spatial References

## Slide 17: Spatial references
Key properties
Coordinate system
  Geographic
  Projected
XY Resolution
XY Tolerance
Notes: The term XY tolerance was introduced in 9.2. Used to be called cluster tolerance.

## Slide 18: Coordinate systems
Geographic (GCS)
Projected (PCS)

## Slide 19: What is a coordinate system?
An agreed upon way to describe locations
Represents locations
  Geographic features
  Imagery
  Observations such as GPS locations
Common geographic framework
Used to integrate geographic locations from different datasets
Notes: How far is Redlands? I don’t expect the answer in feet from Beijing. I expect it in miles from where I am.
I look at a map, expect North at the top. If I am in Australia, I might expect South to be at the top.
Where we are and who we are talking to determines the way a map is presented. That’s a coordinate system.

## Slide 20: Geographic Coordinate System (GCS)
Global – 3D spherical surface
Point referenced by longitude and latitude values

## Slide 21: Projected Coordinate System (PCS)
Flat – 2D surface based on a GCS
X
Y
(0,0)
X > 0
Y > 0
X < 0
Y > 0
X < 0
Y < 0
X > 0
Y < 0
Point referenced by x, y coordinates on a grid

## Slide 22
Datum
Spheroid
Prime Meridian
Projection Parameters
Projection
Projected Coordinate System
Geographic Coordinate System
Coordinate System
Angular Unit
Linear Unit
Notes: Each predefined SR has a coordinate system which can be either projected or geographic.
GCS
  coordinates are longitude and latitude
  on the spheroid, the globe
  Angular units such as degrees or radians
PCS
  inherits or contains a geographic coordinate system
  Is flat on the map
  Linear unit such as feet, meters

## Slide 23: Geographic Coordinate System Well-Known Text (WKT)
GEOGCS[ "GCS_WGS_1984",
DATUM[ "D_WGS_1984",
SPHEROID[ "WGS_1984", 6378137.0, 298.257223563] ],
PRIMEM[ "Greenwich", 0.0],
UNIT[ "Degree", 0.0174532925199433] ]
Notes: Can represent GCS as string.
Datum
  spheroid tells you size and shape, WGS_1984
  semimajor axis, equatorial axis, of the spheroid.
  inverse flattening and tells you how squashed it is versus a sphere.
  Does the surface of the spheroid align well with the entire earth like WGS84? Or should it be used in a particular area like NAD27 is used in North America?
Prime meridian - zero position for the longitude values
Unit – how to convert to radians

## Slide 24: What is a datum?
Notes: Black is surface of earth
Upper left is North America
  local datum fits pretty well in that region
  doesn’t fit well in lower right
Earth-centered datum fits relatively well everywhere
Lat/long different on local vs. earth-centered

## Slide 25: Projected Coordinate System Well-Known Text (WKT)
PROJCS[ “World_Mercator",
GEOGCS[ "GCS_WGS_1984",
DATUM[ "D_WGS_1984",
SPHEROID[ "WGS_1984", 6378137.0, 298.257223563] ],
PRIMEM[ "Greenwich", 0.0],
UNIT[ "Degree", 0.0174532925199433] ],
PROJECTION[ "Mercator " ],
PARAMETER[ "Central_Meridian", 0.0],
PARAMETER[ "Standard_Parallel_1", 0.0],
PARAMETER[ "False_Easting", 0.0],
PARAMETER[ "False_Northing", 0.0],
UNIT[ “Meter", 1.0] ]
Notes: PCS
  GCS embedded in it.
  has a name
  a projection—a link to the mathematical algorithm
  parameters that the projection needs
  linear unit – how to convert to meters

## Slide 26: Well-Known ID (WKID)
Every predefined coordinate system has a WKID
  For example, GCS_WGS_1984, WKID = 4326
WKID < 32767 is EPSG assigned
  EPSG Geodetic Parameter Dataset, http://www.epsg-registry.org/
WKID > 32767 is Esri assigned
  Esri WKID may change
  Esri  EPSG
  Old WKID will still work
  Example, Web Mercator 102100  3857
Notes: Each projection engine object, such as a coordinate system, unit, or spheroid has a well-known id
You may also hear “EPSG code”. The EPSG Geodetic Parameter Dataset contains lists of coordinate systems and transformations and the objects that make them up.

## Slide 27: All projections have some distortion
Web Mercator Projection
Notes: Mercator projection distorts area and distance
See the distortion of Antarctica
South America is actually 7 times bigger than Greenland

## Slide 28
What is happening when we project data?
PCS A2
GCS A
PCS A1
Projection
(lon, lat)
(x, y)
(λ, φ)
Case 1: Both PCSs contain the same GCS
Projection
Notes: What really happens when you project data?
Converting from PCS A1, which is using GCS A to PCS A2, also based on A
Direct projection that takes two steps
  Unproject from A1 to A
  Project from A to A2.

## Slide 29
Geographic Transformation
GCS A
PCS A1
GCS B
PCS B1
Case 2: Each PCS contains a different GCS
What is happening when we project data?
(lon, lat)
(x, y)
(λ, φ)
Projection
Projection
Notes: Output projected coordinate system is B1, based on GCS B.
The 1st step is still to unproject to A.
Then convert latitude and longitude values from GCS A to GCS B. That requires a geographic, or datum, transformation.
Once that’s done, we project from GCS B to PCS B1.

## Slide 30: Geographic Transformations (GT)
Convert from one GCS to another GCS
Suitable for a particular area
Defined in a particular direction
  For example, NAD27 to WGS84
  All are reversible
May be more than one applicable GT
Notes:   A geographic transformation converts between two geographic coordinate systems.
  Lat/long on one ellipsoid may be different on another.
  All transformation methods convert everything that might need to be changed, including the units, prime meridian, and the spheroid.
  Each transformation is always defined in a particular direction, from “A” to “B”, but are completely reversible. In
  ArcMap, we present a list in order of most to least suitable. Normally, you want to use the top entry

## Slide 31: There are 38 transformations between GCS_North_American_1927 and GCS_WGS_1984
Which is best?
Depends on the region covered by your data
Notes: Which is best?
Depends on the region covered by your data

## Slide 32
Why do we need to transform our data?
European Datum 1950 vs. World Geodetic System 1984
Notes: Vector and raster layers
ED50 (European Datum 1950) and WGS84 (World Geodetic System 1984)
Red ellipse – lines up OK
Yellow ellipse – not OK
To fix, transform one of the layers

## Slide 33: Projection between different GCSs
Demo
Notes: Map of US States and Palm Springs with Oceans base map.
Data frame is NAD 83 UTM Zone 5. Add States doesn’t look good.
Change to NAD 83 UTM Zone 14. Same GCS so no transformation.
Now change to Fuller. GCS is WGS 84. ArcMap will ask for transformation. Pick the first one.
Change to Azimuthal Equidistant. Same GCS.

## Slide 34: Resolution and Tolerance

## Slide 35: XY Resolution
Numeric precision used to store x, y coordinate values
All coordinates lie on coordinate grid
Default value is 0.0001 meters or equivalent
  x1 = 5.1234, x2 = 5.1235 stored as unique coordinate values
  x1 = 5.12344, x2 = 5.12345 both stored as 5.1234
  Each square in grid is 0.0001 x 0.0001
Notes: If |x1 – x2| <= res, then stored as same number
Default value in meters. 1/10 millimeter
If SR has feet, then default is 0.0001 m = 0.0003281 ft
Lat/long then 0.000000001 degrees
If developing own app, you have to set xy-resolution probably.

## Slide 36: XY Tolerance
Minimum distance between coordinates when processing features
  Simple geometry validation
  Topological operations such as Buffer
  Relational operations
  Editing operations
Notes: Tolerance comes into play when processing features, not storing them.

## Slide 37: XY Tolerance

## Slide 38: Merge polygons
Demo

## Slide 39: Resolution vs. Tolerance
Resolution: refers to number of decimal places used to store x, y coordinate values
Tolerance: minimum separation between features used by some operations
  Should never be less than 10 times resolution
Default resolution = 0.0001 meter or equivalent
Default tolerance = 0.001 meter or equivalent
Highly recommended to use default values!
Notes: Storage vs. processing

## Slide 40: What do spatial references have to do with geometries?
Geometry is a collection of points
Spatial reference determines
  where the coordinates are placed
  how the coordinates interact with each other

## Slide 41: How does a spatial reference affect a geometry?
We need to know where to put the geometry on the map
A geometry that is simple in one spatial reference may not be so in another spatial reference
Remember, garbage in, garbage out
An operation on features may give different results depending on the spatial reference

## Slide 42: Where on the map do I put the geometry?
Demo

## Slide 43: How does a spatial reference affect a geometry?
We need to know where to put the geometry on the map
A geometry that is simple in one spatial reference may not be so in another spatial reference
Remember, garbage in, garbage out
An operation on features may give different results depending on the spatial reference

## Slide 44: What is simple here may not be simple there
Demo
Notes: This rectangle lives inside one square of tolerance. All 4 vertices are considered the same when checking validity.

## Slide 45: How does a spatial reference affect a geometry?
We need to know where to put the geometry on the map
A geometry that is simple in one spatial reference may not be so in another spatial reference
Remember, garbage in, garbage out
An operation on features may give different results depending on the spatial reference

## Slide 46: An operation on features may give different results depending on the spatial reference
For example, Buffer operation
Notes: Buffer operation
  creates a new geometry such that each point is a given distance from the original geometry.
  Euclidean distance – flat map projection
  Geodesic distance – shortest path on surface of the earth

## Slide 47: Buffer and Spatial Reference
Demo
  Web Mercator Buffer Demo
  Azimuthal Equidistant Buffer Demo
Notes: Red is geodesic buffer, blue is planar buffer
Change where we calculate the buffer

## Slide 48: References
http://resources.arcgis.com/en/help
  Desktop → Guide Books → Map projections
  Developer Help
    List of ArcGIS APIs
Lining Up Data in ArcGIS, Margaret Maher
ESRI Technical paper: Understanding Coordinate Management in the Geodatabase
ESRI Technical paper: Understanding Geometric Processing in ArcGIS

## Slide 49: Resources
ArcMap Demos
  Projection between different GCSs
  Merge polygons
  Where on the map do I put the geometry?
  What is simple here may not be simple there
JavaScript Demos
  Why do we care if geometries are simple?
  Buffer and Spatial Reference
    Web Mercator
    Azimuthal Equidistant
Python Toolbox to convert JSON to GDB
Links for demos, data and more!

## Slide 50: That’s all folks! Don’t forget to fill out the survey Understanding and Using Geometry, Projections and Spatial Reference Systems in ArcGIS